## Slide 1
6G ADVANCED RESOURCE SCHEDULER
Edge Scheduling Engine
A Distributed Systems Approach to 5G/6G
Network Resource Allocation
Raft Consensus
DDPG Reinforcement Learning
Two-Timescale Orchestration
Distributed Systems Course · Group 30 · University of Oulu

## Slide 2
The Problem: One Radio, Three Incompatible Demands
Why static resource allocation fails in 5G/6G
eMBB
Enhanced Mobile Broadband
10+ Gbps DL
Bulk data, video streaming, heavily downlink-heavy
URLLC
Ultra-Reliable Low-Latency
<1 ms latency
Industrial robots, autonomous vehicles — timing critical
mMTC
Massive Machine-Type Comms
1M devices/km²
IoT sensors, bursty small uplink packets
The Clash:
All three services share ONE physical spectrum. They cannot transmit simultaneously — signals collide and destroy each other. A single static policy cannot efficiently serve all three at once. This is the core scheduling problem.

## Slide 3
System Architecture: Three-Tier O-RAN Design
Radio Unit → Distributed Unit → Centralized Unit
☁ CLOUD TIER (CU)
Non-RT RIC · 10 s loop
PySpark Analytics
Orchestrator
QoS Policy Engine
⚡ EDGE TIER (DU)
Near-RT RIC · 100 ms loop
Raft Cluster (3 nodes)
DDPG Agent
Proportional Fair Scheduler
📡 RADIO TIER (RU)
Physical layer · 100 ms sim
Base Station Simulator
20 UEs · path loss · CQI/SINR
Poisson traffic per slice
↕ Policy updates (10 s)
↕ gRPC stream (100 ms)
Two-Timescale Control Loop
Fast Loop — 100 ms
DDPG infers TDD split α
Prop. Fair allocates PRBs
ScheduleDecision → simulator
Slow Loop — 10 s
Spark aggregates telemetry
Orchestrator detects starvation
Pushes QoS weights to DU
Constraint: αDL + αUL = 1 (physics)

## Slide 4
Raft Consensus: Fault-Tolerant Scheduling Authority
Custom zero-dependency implementation · 282 lines · Python
The Problem Without Raft
Two DU nodes both believe they are leader → both issue PRB assignments → same spectrum slot assigned to two UEs → signals collide → nobody gets data
State Machine
FOLLOWER
Passive. Receives heartbeats.
CANDIDATE
Timed out. Soliciting votes.
LEADER
Serves all scheduling requests.
Safety Guarantees
At most one leader per term
Election requires majority votes > ⌊n/2⌋
Log Matching Property
Same index + term ⟹ identical prefix. No divergent histories.
Fault tolerance n = 3
Tolerates ⌊(3−1)/2⌋ = 1 simultaneous failure
Re-election ≤ 300 ms
Scheduling gap bounded. Safer than risking double-allocation.
Election timeout: 150–300 ms (randomized) | Heartbeat: 50 ms | RPC timeout: 100 ms | Cluster: 3 nodes

## Slide 5
TDD Scheduling + DDPG: What the AI Actually Decides
One number per epoch. Everything else is deterministic.
What is TDD?
Same frequency band, alternating direction in time.
Base station and UEs cannot transmit simultaneously —
if both try, signals collide and neither gets data.
αDL + αUL = 1 (always, by physics)
DDPG outputs ONE number:
α̂DL ∈ (0.1, 0.9) → fraction of slots for Downlink
Uplink gets the rest automatically: αUL = 1 − α̂DL
DDPG Decision Pipeline
1
State s_t (4D)
[avg DL buffer, avg UL buffer,
avg CQI, avg SINR] normalized 0→1
2
Actor π_θ(s_t)
4→256→256→1 network
Sigmoid output → rescaled to (0.1, 0.9)
3
Prop. Fair Allocator
Given α̂, splits 100 PRBs across
20 UEs by demand × channel quality
Reward:
r_t = −(DL starving UEs + UL starving UEs) / 10000
Example: α̂ = 0.7 with 100 PRBs
70 PRBs → DL | 30 PRBs → UL | Alice (CQI 12): 6 PRBs = 504 B | Bob (CQI 3): 1 PRB = 21 B

## Slide 6
Big Data Analytics + Two-Timescale Orchestration
PySpark pipeline · Cloud ↔ Edge policy feedback
PySpark Analytics
1. Ingest JSONL telemetry logs (2+ GB per run)
2. Tumbling windows Δw = 10 s
3. Group by slice: eMBB · URLLC · mMTC
4. Compute: avg CQI · total DL demand · PRBs
5. Write slice_stats.csv → Cloud Orchestrator
T̄(s,k) = (1/|Wk|) · Σ_{t∈Wk} Σ_{i:slice(i)=s} d(i,t)
Why Two Timescales?
Fast · 100 ms
· DDPG inference: <1 ms on CPU
· PRB allocation: deterministic math
· Must respond before next epoch
Slow · 10 s
· Raw telemetry too noisy to act on directly
· 10 s window smooths burst noise → real trends
· Cloud can tolerate network round trip
Slow loop sets policy weights. Fast loop executes within them. Never blocking each other.

## Slide 7
Experimental Results
10,000 scheduling epochs · Intel i7 CPU · 3-node Raft cluster · 20 UEs
100.94 ms
Mean scheduling
latency (±0.38ms)
99.8%
PRB utilization
across all slices
≤300 ms
Raft re-election
worst case
10,000
Scheduling decisions
per experiment
Buffer Starvation by Slice
Slice | DL Starv | UL Starv | Avg PRBs
eMBB | 99.7% | 99.6% | 8.8
URLLC | 99.1% | 99.4% | 6.0
mMTC | 0.0% | 97.1% | 1.0
Policy collapse: 99.2% of decisions in α = 10–30% range. Caused by symmetric reward under UL-heavy load. Future: constrained RL.
TDD DL Ratio Distribution
Chart: 
| 10–30% | 30–50% | 50–70% | 70–90%
Frequency | 99.2 | 0 | 0 | 0.8
Raft: Unit tests pass deterministically across 100 runs. Re-election completes within 300 ms upper bound in all tested cases.

## Slide 8
Live System Demo
React dashboard · localhost:5173
[ LIVE DEMO ]
Switch to browser → localhost:5173
Demo Checklist
Network topology
5 RUs → 5 DUs → CU-Core
live utilization on links
Raft Consensus View
Heartbeat logs scrolling
leader term counter
DDPG Training Monitor
Critic loss + reward curves
Train vs Evaluate mode
Inject Workload Spike
Watch Raft log react
DDPG penalizes reward
Slice Allocation chart
eMBB dominates PRBs
mMTC gets minimal share

## Slide 9
Conclusions & Anticipated Q&A
1
Custom Raft
Zero-dependency, 282-line Python. Validated: 100 deterministic test runs. Re-election ≤ 300 ms.
2
DDPG Scheduling
4D mean-field state. CPU-viable inference < 1 ms. Honest finding: policy collapse under symmetric reward.
3
End-to-End O-RAN
6 microservices, gRPC streaming, Spark analytics, React dashboard. 99.8% PRB utilization.
4
Two-Timescale
100 ms edge fast loop + 10 s cloud slow loop. Decoupled — no blocking between timescales.
Anticipated Q&A
Q: Why not fix TDD at 0.5?
Static split wastes capacity when traffic is asymmetric — common in real workloads (eMBB is heavily DL-heavy).
Q: Is Raft overkill for 3 nodes?
3 nodes is minimum for majority consensus (tolerates 1 failure). Demonstrates the algorithm correctly; production uses 5–9.
Q: Why is starvation so high?
Policy collapse to low α means only ~10 DL PRBs shared by 20 UEs. Root cause is reward engineering, not the allocator.
Group 30 · Distributed Systems · University of Oulu · github.com/namvdo/edge-scheduling-engine